## Slide 1
Flight Hazards Associated with Thunderstorms & Weather Radar Interpretation
Joe Jurecka CP ASMEL, IA
National Weather Service Lubbock, TX
SAWS 2015 KLAS

## Slide 2: Outline
Thunderstorm Hazards and morphology
Radar limitations
In flight radar
Radar vs. visual
Avoidance tips
Scenarios

## Slide 3: US Thunderstorm Distribution
Average Number of Thunderstorm Days Per Year
noaa.gov
Notes: The west may look less formidable, but there are traps for both east and west coast pilots who traverse the divide. The storms are often very different beasts. Garden variety storms in the west often have more geospatially diverse hazards.

## Slide 4: Thunderstorm attributes
What is a thunderstorm? Any storm (rain or snow) which produces lightning (IC/CG)
Formed when three ingredients combine Moisture, instability, and a trigger (lift)
Hazards Large hail, tornados, severe icing, severe turbulence, downburst winds, lightning
E.g. don’t even think of flying into one!

## Slide 5: Still thinking of trying?
It just doesn’t often end well!
“The probable cause of this accident was the captain's decision to penetrate rather than avoid an area of severe weather…” Southern Air 242

## Slide 6: How about near a thunderstorm?

## Slide 7: Outflow/Downburst
50+ KT
Winds

## Slide 8: Radar limitations overview

## Slide 9: Radar Limitations
Severe Weather Mode
Storm above or below radar beam

## Slide 10: Radar Limitations
Below Beam Effects

## Slide 11: Radar Limitations
Radar Limitation 1: Rain too Far from Radar Cause 1: Beam Broadening
Rain too far from radar (or too weak with beam broadening)

## Slide 12: Radar Limitation
Radar Limitation 2: Rain Blocked from Radar View
Rain Blocked from Radar View
Terrain blocking

## Slide 13: Radar Limitations
http://confluence.org/dk/all/n56e011/pic10.jpg
Ground Clutter and Super refraction
noaa.gov

## Slide 14: Base Reflectivity (lowest tilt 0.5°)
The intensity displayed is 55 dBZ.

## Slide 15: All radar tilts (0.5° to 19.5°)
max intensity

## Slide 16: Composite Reflectivity
The intensity displayed is 62 dBZ.

## Slide 17
Composite Reflectivity | Base Reflectivity
Yes | No, unless storm is far from radar.
Most times | Most times
Sometimes | Yes
Yes | No
Shows developing storms?
Shows fronts, wind shifts?
Shows fine details like thunderstorm gust fronts?
Blocky appearance?
Composite vs. base reflectivity

## Slide 18: What do you get?
Did everything
update 3 mins
ago?
Likely not!
Update frequencies:
METARs 60m (~H+53)
Composite 4-10 min
Base 2-10 min
Cell movement 4-6 min
Lightning update times often not published!
Composite or Base?
You don’t know what you don’t know
garmin.com

## Slide 19: What do you get?
Understand your timestamps!
4 mins since what?
  Base scan start or
  Base scan finish or
  Mosaic creation or
  When downloaded
Beware of filtering! Filtering means MISSING DATA
Eliminating ground clutter also eliminates outflow boundaries
https://bonanza36.files.wordpress.com/2012/11/img_0295.jpg

## Slide 20: May 23 2011 Ozona, TX
http://www.photos4u2c.net/2011/05/26/the-atmosphere-is-ripe/
Typical GA radar 7°
Typical airline radar 3°
WSR 88D 0.95°

## Slide 21: May 23 2011 Ozona, TX

## Slide 22: May 23 2011 Ozona, TX
May 27? 2011 DRT

## Slide 23: Volumetric Radar

## Slide 24: 18 Jun 2009

## Slide 25: 18 Jun 2009 Haboob
Haboob+C182 = 2 dead
Todd Lindley, NWS

## Slide 26: 18 Jun 2009 Haboob
Texas Tech Atmospheric Sciences

## Slide 27: Deviant Motion

## Slide 28: Some rough guidelines
Know the mean storm motion before departure. This is typically the average of the 3000’-30000’ winds.
Avoid the vicinit all thunderstorms.
Never go closer than 5 miles to any visible storm cloud with overhanging areas, and strongly consider increasing that distance to 20 miles or more.
You can encounter hail and violent turbulence anywhere within 20 miles of very strong thunderstorms.
Do not attempt flight beneath thunderstorms, even when visibility is good, because of the destructive potential of shear turbulence in these areas.
At the first sign of turbulence, reduce airspeed immediately to the manufacturer's recommended airspeed for turbulent air penetration for a specific gross weight (that is, maneuvering speed, or Va).
https://www.faasafety.gov/files/gslac/library/documents/2011/Aug/56397/FAA%20P-8740-12%20Thunderstorms[hi-res]%20branded.pdf

## Slide 29: More rough guidelines
If radar paints "moderate" or "heavy" precipitation (previously Level 2 or Level 3; see box on page 18), maintain at least 20 miles separation from the moderate echoes.
When deviating around storms, maneuver on the upwind side so wind isn't carrying the storm toward you, and to avoid hail that might spew from the anvil top.
Avoid flying under thunderstorm cells themselves, where you may find powerful turbulence and intense rain or hail.
http://www.aviationsafetymagazine.com/airplane/Flying-In-Thunderstorms.html

## Slide 30: Final thoughts
Stay away from thunderstorms and all which emanate from them
Hazards exist well beyond the precipitation echo
Look for surface clues if possible
Know your equipment and what it provides and what it hides
Understand data update characteristics

## Slide 31
Thank you
joe.jurecka@noaa.gov
Joe Jurečka National Weather Service Lubbock, TX

## Slide 32: What would you do?
DFW to AMA

## Slide 33: What would you do?
DFW to AMA

## Slide 34: What would you do?
DFW to AMA